## Slide 1: All Roads Transportation Safety (ARTS) Program
Kevin J. Haas, P.E.
Traffic Investigations Engineer, ODOT
February 26, 2015
Notes: Title slide option 1

## Slide 2: Oregon averages 1800 fatalities and serious injuries per year
Based on 2009-2013 data

## Slide 3
Highway Safety Improvement Program (HSIP) federal funding was traditionally only spent on State Highways, but 50% of Fatal and Serious Injury crashes occur on local agency roads
Notes: “there are 1700 fatalities and serious injuries in Oregon per year”

## Slide 4: MAP-21: major themes for HSIP
Reduce Fatalities and Serious Injuries
    Use a data-driven approach that is blind to jurisdiction
Emphasizes spending on all public roads
Requires Performance-Based Measures (States set targets)
    Fatal and serious injury crashes per VMT
    Number of fatalities and serious injuries
    New roadway data and highway basemap requirements
(Federal HSIP, Section 148 of Title 23)

## Slide 5: Data-driven process
A data-driven approach uses crash data, risk factors, or other data supported methods to identify possible locations to achieve the greatest benefits

## Slide 6: Jurisdictionally blind safety discussions initiated in 2012
ODOT met with representatives from the League of Oregon Cities (LOC) and Association of Oregon Counties (AOC)
    Need for developing a safety program for all public roads
    Memorandum of understanding between ODOT, AOC, and LOC
Agreed to All Roads Transportation Safety (ARTS) program

## Slide 7: ARTS program principles
Select the best projects to reduce fatalities and serious injuries
Address safety on all public roads
Data-driven and blind to jurisdiction
Overseen by ODOT Regions

## Slide 8: ARTS funding principles
Allocations to each ODOT Region based on fatalities and serious injuries on all public roads
Projects focused on fatal and serious injury crash reductions

## Slide 9: Project selection principles
Primarily developed and overseen by ODOT
Regional project selection engages local jurisdictions
Combine projects on state and local roads where possible
Follow principles of practical design

## Slide 10: ARTS program timelines

## Slide 11: Transition program for cities and counties
Developed to bridge the gap between 2013 and 2017

## Slide 12: Transition program
ODOT hired a consultant to facilitate the process in each region
Local Jurisdictions participated in selection of a few key systemic measures in each region
ODOT region staff taking the lead on developing the projects
Projects should be designed and underway 2015-2016

## Slide 13: Transition program funding for cities and counties (2013-2016)
Region | Splits* | Funds
1 | 46.6% | $7,461,665
2 | 27.3% | $4,370,457
3 | 14.6% | $2,333,411
4 | 7.5% | $1,207,972
5 | 3.9% | $626,495
Total |  | $16,000,000
*Splits based on F&A crashes on local roads |  | 

## Slide 14: ARTS program funding begins in 2017
ARTS
Hot Spot
(50%)
Systemic
(50%)
Roadway Departure
(50%)
Intersection
(36%)
Bike/Ped
(14%)
Numbers in ( ) represent approximate funding split (statewide)

## Slide 15: Hot Spot
Using traditional hot spot method, locations with histories of fatal and serious injury crashes will be targeted

## Slide 16: Hot spot countermeasures
Courtesy: FHWA

## Slide 17: Hot spot project selection
A 300% list of potential project locations (for each Region)- prepared by consultant
Data-driven analysis
    ODOT approved screening method using ODOT reported crashes only
    Locations shall have at least one F & A within last five years
    Countermeasures from ODOT CRF List
    Prioritized/categorized based on B/C Ratio (using ODOT method)

## Slide 18: Hot spot project selection
One kick-off meeting per Region
    Discussion on selection process and preliminary results
    Input from participants
    Participants may suggest additional project(s) that are not in the list
Additional analysis and refinement of the preliminary list based on input
Meeting to discuss finalized list of potential projects

## Slide 19: Systemic
Systemic approach will be used for low-cost countermeasures that can be widely implemented to reduce fatalities and serious injuries

## Slide 20: Systemic countermeasures
Courtesy: FHWA

## Slide 21: Systemic countermeasures
Countermeasure | CRF | Crash Type | Typical Cost
Curve Warning Signs with Speed Riders | 13% | All | $500-$700 per sign
Oversize Curve Warning Signs | 18% | All | $500-$600 per sign
Chevrons Placed in Accordance with 2009 MUTCD | 20%-35% | All (dependent on facility type) | $300-$500 per sign
Centerline Rumble Strips | 12% | All Rural 2-Lane Roads | $700-$1000 per mile
Centerline Rumble Strips | 21% | Head on & Sideswipe | $700-$900 per mile
Shoulder Rumble Strips | 22% | All Rural MultiLane/ two lane | $700-$1000 per mile
Profiled Pavement Markings | 10% | All | $1.50-$2.50 per foot
First Time Installation of Delineators Where None Existed Before | 11%/34%/67% | All/Run off Road/ Head-On | 500 ft curve = $210-$420 1,000 ft curve = $270-$540

## Slide 22: Systemic projects
Shall not require acquisition of a significant amount of ROW
Should have a history of F & A and preferably used on priority corridors from Systemic Plans

## Slide 23: Systemic projects
Application-based selection
ODOT and Local Jurisdictions within a Region will submit applications
Regions will process the applications and prepare a 150% list
Multi-discipline assessment to verify the solution

## Slide 24: Systemic project selection
Three pots of money
Regions have flexibility to determine the split, but should roughly be equivalent to the proportion of F & A within the Regions

## Slide 25: Systemic projects
Intersectional
1,239 fatalities and serious
injuries
48%
Roadway Departure
801 fatalities and serious injuries
31%
21%
Chart: 
Column1 | 31 | 69
Chart: 
Column1 | 31 | 69
Chart: 
Column1 | 21 | 79
Ped/Bike
544 fatalities and serious injuries
Based on 2009-2013 data
Region 1 fatalities and serious injuries

## Slide 26: Systemic projects
Based on 2009-2013 data
Region 3 fatalities and serious injuries
Intersectional
304 fatalities and serious
injuries
Chart: 
Column1 | 10 | 79
Chart: 
Column1 | 65 | 35
65%
Roadway Departure
786 fatalities and serious injuries
25%
10%
Ped/Bike
125 fatalities and serious injuries
Chart: 
Column1 | 25 | 75

## Slide 27: Systemic application process
ODOT has developed application process and forms
    Countermeasures from approved ODOT CRF List
    Based on B/C Ratio or Cost-Effectiveness Index
ODOT will provide technical assistance, if asked
http://www.oregon.gov/ODOT/HWY/TRAFFIC-ROADWAY/Pages/ARTS.aspx

## Slide 28: HSIP funding
A federal reimbursement program NOT a federal grant program
Requires a 7.78% non-federal cash match
92:8

## Slide 29: ARTS funding- statewide (2017-2021)

## Slide 30: ARTS funding- regions (2017-2021)

## Slide 31: ARTS funding by ODOT Region (2017-2018)
Region 1
$12.1 M
Region 2
$12.7 M
Region 3
$5.5 M
Region 4
$4.3 M
Region 5
$2.4 M
Based on 2007-2011 crash data

## Slide 32: ARTS funding- Region 1 (2017-2018)
Based on 2009-2013 crash data
Program | Funding per year (in millions)
Hot Spot | $6.0
Systemic | 
Roadway Departure | $1.9
Intersection | $2.9
Ped/Bike | $1.3
Total | $12.1

## Slide 33: ARTS funding by ODOT Region (2019-2021)
Region 1
$10.2 M
Region 2
$10.4 M
Region 3
$4.9 M
Region 4
$3.2 M
Region 5
$2.1 M
Based on 2009-2013 crash data

## Slide 34: ARTS funding- Region 4 (2019-2021)
Program | Funding per year (in millions)
Hot Spot | $1.61
Systemic | 
Roadway Departure | $1.08
Intersection | $0.42
Ped/Bike | $0.11
Total | $3.21
Based on 2009-2013 crash data. All splits are approximate.

## Slide 35: Where are we?

## Slide 36: Where are we?
Working on
300% List
Draft 300% List/Meeting with Local Agencies
Address Comments, Review Proposals, Refined 300% List
Final 300% List
Draft 150% List
Final 150% List
Scoping
Draft
STIP
Feb Mar Apr May Jun Jul Aug Fall 2016
2015
Hot Spot
Systemic
Application Deadline
Scoping
Draft
STIP
March 27

## Slide 37: Questions about ARTS? Contact your ODOT Region ARTS representative
Sue D‘Agnese (503) 731-3427
Angela Kargel (503) 986-2656
Shyam Sharma (541) 774-6335
Joel McCarroll (541) 388-6189
Ext 239
Jeff Wise (541) 963-1902
http://www.oregon.gov/ODOT/HWY/TRAFFIC-ROADWAY/Pages/ARTS.aspx